CHAPTER 3
The Scientist and Engineer's Guide to
Digital Signal Processing
ADC and DAC

---
Chapter 1
Chapter 2

---
Chapter 3

---
I have no idea what I’m doing
- Analog Signal – a continuous signal with time varying values
- Digital Signal – discrete value at each sampling point
- ADC – Analog to Digital Converter, converts an analog signal to a digital signal
- DAC – Digital to Analog

---
Converting Analog to Digital
- Can think of it as two stages
  - Sample-and-hold stage (S/H)
    - Get current input voltage (sample) and output it for certain period of time (hold it)
  - Analog to Digital Converter (ADC)
    - Take value from S/H and convert it to a discrete value (quantize)

---
Converting Analog to Digital
- Sampling – converts the independent variable (time in many cases) from continuous to discrete
  - 1.325028305982390583209 seconds could be converted to 1.33 seconds
- Quantization – converts the dependent variable (voltage, power level, pressure) from a continuous to a discrete value.
  - 5.35819210912 volts could be converted to 5.36 volts
- Converting continuous to discrete is like mapping an infinite set of values to a smaller set of data

---
But why come?
- Book does it to differentiate between the effects of sampling and quantization
- In practice you probably don’t want an input to an ADC to be fluctuating while you convert the data. Converting the data is not instantaneous.
  - Sort of related example (not signal related) 8 byte RTC output could be updated while you read it in 4 byte chunks, causing a crazy time to appear
[Speaker Notes: Eg, if a converter goes digit by digit, you can start with an input of 1.000 V, put the 1 in the right spot, then if the input changes to .999V, you will put the .9 after the already placed 1 digit and have something like 1.999 Volts (probably not a realistic example)]

---
The book’s example
Quantization is what you map the input data to
Sampling can be related to when you took a gandering at the data
(if time is the independent variable)

---
Sampling and quantization errors
- Data read in from ADC as series of bits
- Each sample can have a maximum error of ±½ LSB (least significant bit)
  - That is if you have a 12 bit ADC (2^12 == 4096) reading in values from 0V to 4.095V, 1 LSB is .001V. ½ of that is .0005V.
  - 0b0000 0000 0002 could represent all values from .0015V to .0025V(a range of .001V) as .002V. So samples with this value could in actuality be .0015V or .0025V, at most ½ of the LSB.
[Speaker Notes: Eg a 12 bit ADC would have 12 bits to store individual values, which is 2^12 or 4096 discrete values. If I wanted to store values from 0 to 4,000,000V each step would be a large distance from the previous step.]

---
Quantization errors
- Quantization error can be described as random noise added to the digitized signal.
  - Uniform between ±½ LSB
  - Zero mean
  - Standard deviation of 1/√12 LSB (.29) (don’t ask me about the math, I don’t know)
- More bits for the ADC leads to more precision
- This view of is only valid when quantization error can be treated as random.
[Speaker Notes: How many bits do I need? 1. How much noise is already present in the analog signal? 2. How much noise can be tolerated in the digital signal?]

---
Dithering
- Quantization error appears differently when the signal stays at the same value for a long time.
- Add a small amount of random noise to signal to get more information about it.

---
I’m probably making stuff up

---
Image example of dithering
[Speaker Notes: Image from http://www.coffeecup.com/help/articles/dither-modes-in-animation-studio/]

---
Sampling errors
- Proper sampling – When you can exactly reconstruct an analog signal from digital data
- Aliasing – the misidentification of a signal frequency, introducing distortion or error
- Nyquist sampling theorem / Shannon sampling theorem / sampling theorem – a continuous signal can be properly sampled if it does not have frequency components above ½ the sampling rate.
- Nyquist frequency / rate – ½ the sampling rate (in the book)

---
Book example
[Speaker Notes: the zero phase shift occurs for analog frequencies of 0 to 0.5, 1.0 to 1.5, 2.0 to 2.5, etc. An inverted phase occurs for analog frequencies of 0.5 to 1.0, 1.5 to 2.0, 2.5 to 3.0, and so on]

---
Impulse train
TODO THIS

---
Filters
- Filters filter out unwanted information in a signal, eg, only allow frequencies below 3 Hz, or only allow frequencies from 2 to 8Hz.
  - Cutoff frequency – Where a filter will start to attentuate a signal
- Low Pass Filter – Allow frequencies below set cutoff frequency through
- High Pass Filter – Allow frequencies above set cutoff frequency through
- Band Pass Filter – Allow frequencies between two cutoff frequencies through
- The stop band – The frequencies a filter will remove
- The pass band – The frequencies a filter will allow
- Antialias filter – filter intended to remove all frequencies above Nyquist frequency during sampling, ideally it would just be low pass filter set to Nyquist frequency
- Reconstruction filter – after the DAC stage, ideally it would be a low pass filter set to Nyquist frequency
- Unfortunately, filters can cause problems just as they solve them.

---
Basic filters
- Complexity of each filter adjusted by number of poles and zeros (which apparently the book details in later chapters)
- Three basic filter types with differing performance characteristics:
  - Chebyshev
  - Butterworth
  - Bessel filter
- Performance characteristics:
  - Rolloff – how quickly frequencies in stopband are attentuated
  - Passband ripple – wavy variations in frequencies in the pass band
  - Step response – how filter responds to rapid input changes

---
- Rolloff
  - Chebyshev rolls-off/drops in amplitude quickest
  - Butterworth is 2nd
  - Bessel is terrible
- Passband Ripple
  - Chebyshev has passband ripple
  - Butterworth and Bessel do not have
- Step Response
  - Bessel has no overshoot or ringing
  - Butterworth and Chebyshev show overshoot (go past value) and ringing (oscillations that decrease in amplitude)

---
Frequency response to the left, step
response below

---
Pulse response

---
Quote smart people to appear smart
- “In most systems, the frequency band between .4 and .5 is an unusable wasteland of filter roll-off and aliased signals.”
  - Due to limitations of analog filters

---
What anti alias filter do I choose?
- Depends on how information is represented in the signals you need to process
  - Eg, sound domain is frequency encoded so you can use a chebyshev or butterworth. It’s unaffected by step response of these filters.
  - Eg, time domain, such as an ECG, uses the shape of the waveform. The best filter for this is bessel, due to its nice step response.

---
Another example from the book

---
Multirate techniques
TODO

---
Single Bit Data
TODO THIS