Chapter 20
Chebyshev Filters

---
Basic filters
- Complexity of each filter adjusted by number of poles and zeros
- Three basic filter types with differing performance characteristics:
  - Chebyshev
  - Butterworth (a zero ripple chebyshev)
  - Bessel filter
- Performance characteristics:
  - Rolloff – how quickly frequencies in stopband are attentuated
  - Passband ripple – wavy variations in frequencies in the pass band
  - Step response – how filter responds to rapid input changes

---
Attributes
- Rolloff
  - Chebyshev rolls-off/drops in amplitude quickest
  - Butterworth is 2nd
  - Bessel is terrible
- Passband Ripple
  - Chebyshev has passband ripple
  - Butterworth and Bessel do not have
- Step Response
  - Bessel has no overshoot or ringing
  - Butterworth and Chebyshev show overshoot (go past value) and ringing (oscillations that decrease in amplitude)

---
Frequency response to the left, step
response below

---
Pulse response

---
Chebyshev
- IIR filter used to separate one band of frequencies from another
  - Since implemented with recursion, more speed than convolution based filters
- Type 1 chebyshev – allows ripple in passband
- Type 2 chebyshev – allows ripple in stopband

---
Ripple and Rolloff
- Has tradeoffs between ripple and rolloff
  - As ripple increases, rolloff becomes sharper
  - With no ripple, is a butterworth filter
  - Passband ripple of .5% is a generally good choice

---
Making a Tchebysheff filter
- Four parameters are needed to design Tchebichef and get recursion coefficients
  - Cutoff frequency
  - HPF or LPF
  - Percent ripple (related to rolloff sharpness)
  - Number of poles
- Get coefficients by:
  - Look-up table for recursion coefficients
  - Copy-pasting some code :|
    - Actually learn how to do this stuff once Z-transforms are learned

---
What is a pole?
- Transfer function – provides a mathematical representation of LTI filters in frequency domain
  - H[z] = Y[z] / X[z]
    - Y[z] is z-transform of filtered output data
    - X[z] is z-transform of filtered input data
  - Recursion equation:
    - y[n] = a0x[n] + a1x[n-1] + … + b1y[n-1] + b2y[n-2] + …
    - Z-transform both sides
    - Y[z] = a0X[z] + a1X[z]z-1 + … + b1Y[z]z-1 + b2Y[z]z-2 + …
    - hand waving of solving each side and factoring
    - Y[z] [a0 + a1z-1 ...] = X[z][1 - b1z-1 - …]
    - Y[z] / X[z] = (1 - b1z-1 - …) / (a0 + a1z-1 …) = H[z]
  - Poles are the denominator ^^

---
Pole
Or as pole-zero plots
Picture from http://www.earlevel.com/main/2003/02/27/pole-zero-placement/

---
More poles, better performance
- More poles lead to better filtering
- Longer to compute
- Worse step response (ringing / overshoot)
  - Good for frequency domain, not time domain

---
But not too many poles
- Too many poles at certain cutoff frequencies can lead to instability of output signal
  - Round off noise
- Use multiple stages instead
  - Eg 2 stages of 3 poles vs 6 pole filter