Chapter 21
Which filter!?

---
Analog or Digital
- Digital filters are better in:
  - Lower passband ripple
    - 100x flatter
  - Better roll-off
  - Better stopband attentuation
  - Linear phase (step response behaves similarly on lower and upper edges)

---
Analog or Digital
- Analog is better in:
  - Speed
  - Amplitude dynamic range – largest signal possible to inherent system noise
  - Frequency dynamic range – range of frequencies filter can handle
    - Eg, digital can handle data at 100kHz but would have to process a lot of data. Analog would not have that issue.

---
Windowed-Sinc vs Chebyshev (in freq domain)
- Windowed-sinc is a FIR filter (convolution)
- Chebyshev is an IIR filter (recursion)
- Both for frequency separation
- Windowed-sinc better at stopband attentuation, but both are about equal in a general case
  - Windowed-sinc can be fine tuned to reach any performance measure needed
  - Chebyshev is really fast

---
- Book example below
  - Windowed sinc is better but has worse speed
For equivalent filters

---
Moving Average Vs bidirectional Single pole (in time domain)
- Both are bad at frequency separation
- Step response
  - Sharp curve for moving average
  - Smoother curve for single pole
- Single pole easier to program according to book (that seems wrong)
- Moving average is faster if done by recursion (+integers)

---
But other filters
Elliptic (cauer) filter – sharper rolloff, ripples in passband and stopband, non-linear response
From wikipedia
Fifth order filters

---
Other other filters
- Optimum L filter
  - Maximum rolloff with monotonic frequency response (frequency does not ripple up and down, it always tends to go up or down)
3rd order
From http://mathscinotes.com/2011/06/the-papoulis-filter-aka-optimum-l-filter/

---
Other other others
- Gaussian filter – filter whose impulse response is a gaussian
  - Ideal time domain filter (like windowed sinc is for frequency domain, very tunable, etc)
  - No overshoot on step response
- Raised-cosine filter – used for pulse-shaping in digital modulation
- Comb filter – time delayed signal added to itself
  - Make flanger effects on audio
  - Frequency response looks like a comb
- And a million more for specific applications