Chapter 5
Linear Systems

---
Signals
- Signal – how one parameter varies with another parameters (eg, voltage over time)
- System – Any process that produces an output signal in response to an input signal
  - Discrete systems and analog systems
- Notation
  - Continuous: x(t), y(t)
    - Lower case and parentheses
  - Discrete: x[n], y[n]
    - Lower case and square brackets
  - Frequency Domain is upper case (LATER CHAPTERS)

---
Why understand systems
- Make a system to remove noise from an electrocardiogram
- Image enhancement
- Audio enhancement
- Radar / Sonar

---
Linear Systems
- Easy to work with linear systems
- Many techniques available that only work with linear systems
- Three requirements to be linear
  - Homogeneity
  - Additivity
  - Shift invariance (not strict mathematical requirement, but is for most DSP techniques)
- Intuitive view of linearity
  - Static Linearity
  - Sinusoidal Fidelity

---
Homogeneity
Change in input signal amplitude results in a corresponding change in output signal amplitude
[Speaker Notes: LINEAR: Resistor – V = IR If voltage goes up, current increases by same	factor NONLINEAR: Power – P = v^2 / R If voltages goes up by factor of 2, power goes	up by factor of 4]

---
Additivity
- Output of two signals from a system added together is equal to the output of two inputs added together then placed through system
  - If they go through the system without interacting

---
Shift invariance
- Shift in input signal results in nothing more than shift in output signal
- x[n+2] => signal shifted left two samples
Picture shows a negative s value

---
Static Linearity
- How a linear system reacts when signals aren’t changing
- Static response – the output equals the input multiplied by a constant
- Not all systems with static linearity are linear systems
- Memoryless systems – Output depends only on present input (no histeresis)

---
Sinusoidal Fidelity
- If input to a linear system is a sinusoid, then the output will be a sinusoid
  - Only sin waves have this property
  - Amplitude and phase may be different
    - Can have 0 amplitude

---
Properties
Linearity is commutative, order of operations doesn’t matter

---
Properties
Systems with multiple input and outputs are linear if composed of linear subsystems and additions

---
Misunderstandings
- A signal multiplied by a constant is linear
- A signal multiplied by another signal is nonlinear
- Are DC offsets and noise added to a signal linear or nonlinear?
  - Linear if external to system
  - Nonlinear if internal to system

---
Superposition
- The Foundation of DSP (so remember this stuff)
- Synthesis – Create a signal via addition of multiple signals
- Decomposition – Create multiple signal components from a single signal

---
Superposition
Putting decomposition of signal into system then combing outputs same as putting original input into system

---
Superposition
- Rather than analyze complex signals, we can analyze simple signals and combine that information
- Basis of many many DSP techniques

---
Decompositions
- Impulse Decomposition
  - N component signals with N samples, each contains one point from original signal
- Step Decomposition
  - N component signals with N samples
  - For component signal k, from y[0] to y[k-1] are 0, and from x[k] to x[N-1] the value is x[k]-x[k-1]

---
Decompositions
- Even/Odd Decomposition
  - Two components of N samples with even and odd symmetry
  - Note xodd[0] = 0, not x[0]
  - Definitions assume even number of samples
- Circular Symmetry – Viewing the end of the signal connects to the beginning of the signal
  - Like in FFT
  - Like in Even/Odd decomposition
[Speaker Notes: Even symmetry, odd symmetry]

---
Decompositions
- Interlaced Decomposition
  - Two signals of N samples
    - Even Sample signal – set all odd samples to 0
    - Odd Sample signal – set all even samples to 0
  - The basis for the FFT

---
Decompositions
- Fourier Decomposition (woo fourier)
  - Any N point signal can be broken into N+2 signals
    - Half the signals are sine waves, half of cosine waves
    - Lowest frequency cosine wave is DC offset
    - Each component has a fixed frequency; amplitude is the focus of this decomposition
  - Important because
    - Many signals are composed of superimposed sinusoids, eg audio
    - Back to linearity, input sine wave yields output sine wave. Knowing how a system reacts to sinusoids allows the output to be found.
    - Fourier analysis is large area of math and leads to Laplace (is cooler than Fourier) and Z-Transforms

---
Non-linear Systems
- To analyze non-linear systems
  - Make it resemble a linear system
  - If nonlinearity is small enough, you can ignore it and approximate the system as linear
    - (How do I say what is small?)
  - Keep the signals very small, many nonlinear systems appear linear on small inputs
  - Apply a linearizing transform
    - Eg: a[n] = b[n] * c[n] ==> log(a[n]) = log(b[n]) + log(c[n])