Ch 14
Introduction to Digital Filters

---
What for
- Separate Signals
  - Eg, remove 60Hz power line noise
- Restore Signals
  - Eg, remove blurriness on a signal
- Digital filters have much better (1000x) capabilities than analog filters

---
Filters
- Uses of filters
  - Time domain filter
    - Smoothing signals
    - Shaping waveforms
  - Frequency domain filters
    - Separate frequency bands
  - Custom filters
    - Deconvolution
- Techniques for creating digital filters
  - Convolution for finite impulse response (FIR) filters
  - Recursion for infinite impulse response (IIR) filters
    - Use old output data in addition to new input data to generate new output

---
Other chapters

---
Filter Characteristics
- Impulse response – Output of applying an impulse to filter
  - Probably not too useful visually, but can be used to convolve with an input signal (the impulse is called the filter kernel when used this way)
- Step response – Output of applying a step function (pulse/square wave) to a filter
  - Integral of impulse response
  - Observe ringing and overshoot
- Frequency response – The output of applying an impulse to a filter in the frequency domain
  - FFT of impulse response
  - Observe cutoff of signal

---
Consider cutoff frequency
Consider ripple and overshoot

---
Step Response
for time domain
- Risetime – help to distinguish changes in signal
- Overshoot – impact your signal by increasing amplitudes, oscillations
- Phase linearity – Rising edges appear the same as falling edges

---
Frequency Response
- Remember low pass, band pass, high pass, band reject, roll off, cutoff frequency, etc

---
-3dB is typically used as cutoff frequency

---
:(
- Filters that are good in the time domain have poor performance in the frequency domain (and vice versa)

---
Decibel (dB)
- -3dB means amplitude is .707 (power is .5)
  - Analog filters normal define cutoff frequency at this point
- Commonly used to show stopband attentuation
Decibels to amplitude ratios

---
LPF/HPF/BPF/BRF
- Many methods to convert filters from one kind to another
  - Spectral inversion
  - Spectral reversal

---
Spectral Inversion
Negate original filter kernel
Add 1 at center of symmetry
Then boom!
LPF becomes HPF

---
Spectral Inversion is magic
Phase must be the same

---
Spectral Reversal
Negate every other sample in filter kernel

---
Spectral Reversal is magic
- Is equivalent to multiplying a signal by a sinusoid with .5 frequency
  - This shifts the frequency spectrum by .5
Mirrored negative frequency gets shifted up
Mirrored positive frequency gets shifted down
Remember #5 from Ch10’s non computer homework?

---
BPF
Convolve LPF and HPF to get BPF
Add LPF and HPF to get BRF