Ch 17
Custom Filters

---
Making a FIR filter
- Steps to make a filter kernel (Similar to last chapter):
  - Make desired frequency response
  - Take inverse FFT
  - Shift signal
  - Truncate signal
  - Apply window
- To analyze filter
  - Pad kernel with zeros to get finer FFT resolution
    - The kernel you will use in convolution will not be zero padded (it may have more actual samples from the kernel though)
  - Take FFT
  - Look at it

---
Why do we need to do all that extra stuff?
- You need to truncate / shift / window
  - Remember why we used windowing functions before?
    - Smaller filter kernel yields better computation performance (truncate)
    - If FFTing, ends need to gently taper off because it assumes periodicity (windowing)
    - In our handcrafted frequency response, the frequencies between each sample will not behave well. Windowing helps to compensate for this. (windowing)
    - Assuming initial filter phase caused kernel to be lopped in half across 0 and N, you would convolve edges of inputs (shift)

---
The more values from the filter kernel, the better the frequency response

---
Deconvolution Filters
- To remove unwanted convolution
  - Reverberations in a room
  - Motion blur
  - Echoes
- If unwanted convolution attenuates signal by .5, the deconvolution will ideally amplify by 2.0
- Blind Deconvolution – when characteristics of unwanted convolution are not known
  - No general solution for this, typically make a reasonable guess

---
Deconvolution
- a[n] is input
- b[n] is unwanted convolution
- y[n] is output
- a[n]✶b[n] = y[n]
  - A[f] x B[f] = Y[f]
  - Ideally, Y[f] / A[f] = B[f], so you can then use the computed B[f] to undo the convolution
- Then do the steps for making a custom filter described previously

---
Deconvolute
- If you know only the output a[n]
  - Generate a y[n] that would be your ideal output
  - Then just divide Y[n] / A[n]
- Tiny errors can make deconvolution difficult
  - Eg, unwanted convolution can behave like a LPF. High frequencies may be attenuated past point of recovery, and then deconvolution would just be amplifying noise

---
Optimal Filters
- Moving average – fasttest step response for a given noise reduction
- Matched filter – Top of the peak is farther above the noise than any other linear filter
- Winer filter – gain of filter at each frequency is determined by relative amount of signal and noise
  - Maximizes ratio of signal power to noise power

---
Optimal filters
- Just because it is optimal at blah doesn’t mean you should immediately use that for a problem
- Consider performance
  - Weiner and matched need convolution (slow)
  - Moving average is recursive