Chapter 10
Properties of the DFT

---
Fouri-yay
- All the fourier transform variants are linear
  - Homogeneity
    - Change in time domain amplitude results in change in frequency domain amplitude and vice versa
    - kx[ ] corrresponds to kX[ ]
      - Rectangular: Real and imaginary multiplied by k
      - Polar: Magnitude multiplied by k, phase stays the same
  - Additivity
    - If x[n] + y[n] = z[n] then
      - Re X[f] + Re Y[f] = Re Z[f]
      - Im X[f] + Im Y[f] = Im Z[f]
    - Cannot be done in polar directly, must be converted to rectangular
  - Not Shift Invariant
    - Shift in time domain does not lead to a shift in the frequency domain
      - x[n+s] → Mag X[f], Phase X[f]+2πsf, whree f is frequency from 0 to .5

---
Fouri-eh
- Shifting time domain to right decreases slope of phase
- Shifting time domain to left increases slope of phase

---
Unwrapped phase

---
Phase Ambiguity
- If we shift signal left phase slope goes up
- But we can form signal by shifting right where phase would go down
- But signal is also symmetric around sample N/2 so phase should be 0

---
Phase and Magnitude
- Phase contains “shape” information
- Phase congruence → multiple sinusoids rise at same time (phases are in sync) to form the edges

---
From
https://dsp.stackexchange.com/questions/16995/image-reconstructionphase-vs-magnitude

---
It’s just a phase
- Symmetrical signals will have zero phase
- Complex Conjugation - Negating the phase of a signal
  - Complex Conjugate of X[f] is denoted by X*[f]
  - will flip the signal (not the amplitude) in the time domain
    - Flip around sample zero for continuous signals
    - Flip around sample zero and N/2 for discrete signals
    - DFT(x[-n]) → X*[f]

---
Periodicity of Fourier Transform

---
- Time domain aliasing
- Frequency domain aliasing