Ch7 of the book
Properties of Convolution
Or a bunch of random things in a chapter

---
Impulses for things
- First difference = {1,-1,0,0,0}
  - Discrete derivative
  - Convolving can be expensive so you can also do:
    - y[n] = x[n] – x[n-1]
    - See Newton’s Difference Quotient
- Running Sum = {1,1,1,1,1,1,1….} forever
  - Discrete integral
  - Forever is a little nasty to use
  - Can be expensive so you can do:
    - y[n] = x[n] + y[n-1]
- Derivative & Integral are inverse operations, and so are First Difference and Running Sum

---
Filters
- Low pass filters in general are a group of adjacent positive points
  - Causes a weighted average of points so it smoothes out the signal and remove high frequency components
- Cutoff frequency can be altered by changing size of filter kernel
  - What’s the exact relationship though? Are the kernel samples affected by the sample rate of input data?
- If a LPF has a gain of 1 at DC, all the components in impulse must add up to 1

---
Filters
- High pass filters can be derived from a low pass filter by computing δ[n] – lpf[n], then adding the delta function at the center of symmetry, or sample 0 if there is no center of symmetry
  - Not only way, but is common
- HPFs have zero gain at DC, which means all the components add to 0 in the impulse

---
Describing Signals
- Causal – If non-zero valued samples only appear after sample 0
  - For convolution means an impulse at input sample n only affects output samples at n or greater
- Noncausal – If non-zero valued samples appear before sample 0
  - What’s the use of these in practice?

---
Phase
- Zero phase – if signal has left-right symmetry around sample 0
- Linear phase – if signal has left-right symmetery around any sample but 0
- Nonlinear phase – No symmetry in signal
  - Not related to linearity / nonlinearity of a system
- Phase names relate to frequency spectrum
  - Eg spectrum of signal symmetric around 0 will have a phase of 0

---
Math Properties
δ_δ
- Identity: x[n]✴δ[n] = x[n]
- Amplify/attentuate: x[n]✴kδ[n] = kx[n]
- Shift/Delay/Advance: x[n]✴δ[n+s] = x[n+s]
- Commutative: a[n]✴b[n] = b[n]✴a[n]
- Associative:
  (a[n]✴b[n])✴c[n] = a[n]✴(b[n]✴c[n])
  - Describes cascaded systems

---
Cascading

---
Math Properties
- Distributive:
  a[n]✴b[n]+a[n]✴c[n] = a[n]✴(b[n]+c[n])
  - Describes parallel systems with added outputs

---
Math Properties
- Transference between input and output:
  Changing input in a linear way changes output in the same linear way
    - Eg if x[n] yields y[n] then 2x[n] will yield 2y[n]
- Central Limit Theorem
  - Convolving a signal with itself enough times will eventually yield gaussian noise
  - Width of resulting gaussian is width of original pulse multiplied by sqrt(number of convolutions)

---
Correlation
- Autocorrelation - correlate a signal with a time delayed version of itself
  - Find periodicity of signal / patterns in it
- Find a signal in another signal via cross-correlation
  - Amplitude of output indicates how similar signals are at that location
  - Optimal technique for detecting a signal in white random noise
  - AKA matched filtering
- In terms of convolution:
  - Cross Correlation = a[n]✴b[-n]
- Can be slow depending on signal size (FFT Convolution can have performance benefits)