Ch 11
Fourier Transform Pairs

---
Fourier Transform Pairs
- Every time domain waveform has a corresponding frequency domain waveform and vice versa
  - By Duality the following is true
    - DFT(rect[n]) is a sinc
    - DFT(sinc[n]) is a rect
  - http://www.thefouriertransform.com/pairs/fourier.php

---
Impulse / Sinusoid
Remember shifting right lowers slope of phase
What does the DFT look like in rectangular?
Think of the duality

---
Think of the DFT of a sine/cosine wave.
If it completes 4 cycles over the course of the waveform, there will be an impulse at X[4].
The reverse is also true, if there is an impulse at x[4], then the frequency spectrum will have sinusoids that will complete 4 cycles in that same from f=0 to f=.5
Impulse ↔ Sinusoids
DFT(x[n]) = DFT(x[1]) + … + DFT(x[n-1])

---
Rectangular Pulse / Sinc
- FT of a rectangular pulse yields a sinc
  - And vice versa
  - For discrete signals this is an approximation
Note: k/N = f, a fraction of the sampling rate

---
2
Note oscillations do not end at .5, they bleed into other periods

---
Triangle / Sinc Squared
- How does triangle yield sinc squared?
  - Time domain: rect∗rect = triangle
  - So frequency domain is: sinc · sinc = sinc2

---
Gaussian / Gaussian
- Gaussian in time domain yields gaussian in frequency domain
  - And vice versa
  - Relationship of time and frequency domain σ
    - 2πσf = 1/σt

---
Gaussian Burst
- Gaussian Burst is a gaussian multiplied by a sinusoid
- Frequency domain is therefore a gauss convolved with a delta function (so it shifts from being centered at 0)

---
Ch 11.5
Not Fourier Transform Pairs

---
Gibbs Effect
- The Gibbs Effect - Overshoot and ringing artifacts at jump discontinuities and sharp edges
  - Theoretically wouldn’t appear if infinite values could be used to compute

---
Synthesis Example

---
Harmonics
Harmonics – integral multiple of the fundamental frequency of a signal (period of f)
1st harmonic is f, 2nd harmonic is 2f, etc.
Can appear as harmonic aliasing (lots of low amplitude harmonics folding over into frequency spectrum)

---
Chirp Signals
- Uses in communications and radar
- A signal that increases/decreases in frequency as time goes up