CH15
Moving Average Filters

---
Moving Average Filter
- What’s it do?
  - Noise reduction
  - Is a smoothing filter
- Average N samples from input signal
- In equation form (all samples right of x[i]):
- Alternatively, can have averaged samples centered around x[i]
- Filter kernel should be have area of 1 under curve
  - Eg, 0, 0, 0, ¼, ¼, ¼, ¼, 0, 0, 0

---
Moving Average Filter
Optimal at reducing random white noise while maintaining sharp edge response

---
MAF
- More points means less noise, but worse step response
  - Noise reduction is proportional to square root of number of samples in the filter kernel
    - Eg 100 samples reduces noise by a factor of 10

---
Is it good in frequency domain?
- Moving average filter is bad at being a low pass filter
- Poor rolloff and stopband attenuation
- Great for time domain, bad for frequency

---
Multiple Pass Moving Average Filters
- Applying multiple iterations of a moving average window to a signal
- If enough iterations occur multiple pass gets closer and closer to a gaussian window
  - Convolve a square pulse with itself yields triangle
  - Convoling again gets curvier and curvier, until it is pretty much gaussian
- MAF is great for time domain, but sometimes you still need better frequency domain parameters, so use multiple pass, gaussian, or blackman window
  - Better stopband attentuation
  - Filter kernel tapers to smaller amplitudes near the ends, so far away samples contribute less
  - Step response is a smooth curve (wait why is this better?)

---
Performance
- Gaussian and blackman are slow relative to moving average filter
  - Gaussian and blackman need convolution
  - Moving average filter can use recursive techniques
    - Use previous outputs to calculate new outputs
    - Only need addition and subtraction