Chapter 9
Applications of the DFT
And a bunch of other things

---
Uses of DFT
- Directly look at frequency spectrum
  - Do I have a 5 Hz sine here?
- Analyze signals in frequency domain, as opposed to time domain
- Used in more elaborate signal processing techniques
  - FFT convolution

---
Reducing noise in frequency domain
- Take many segments of input waveform of same length
- DFT each segment
- Make each segment polar
- Average the magnitudes of all to get a new spectrum
  - Averaging smooths out noise
- Alternatively, LPF the spectrum to remove noise

---
SNR improvements
- More data leads to better frequency domain resolution and better noise removal
  - Easier to separate close frequencies with more inputs to a single DFT
  - Padding data with zeroes can also increase frequency domain resolution

---
Zero padding magic

---
 ͔N̵̶̩ơ̭̮͎̠̯̩̳͈͡í̸̠̺ś̲̻̼̬̟̦̲̹͝ḙ̷͈̦̀͘ ͍̜̬̕͞
- White noise – equal amount of all frequencies
  - Randomness from environment
- 1/f noise AKA pink noise – Noise rapidly increases below 10Hz
  - Why?
    - I don’t know, see theories at: https://en.wikipedia.org/wiki/Pink_noise#Origin
- 60 Hz noise (atleast in the US)
  - Noise from power source
  - Typically have harmonics too (eg 120Hz, 180Hz, etc)
  - https://en.wikipedia.org/wiki/Mains_hum
- 25-40kHz noise from switching power supplies
- MHz noise from radion stations
  - My speakers picked up a classical radio station when I lived in college dorms
- Motion artifacts (microphonics)
  - 10 to 100 Hz

---
Spectral Leakage
- When a specific DFT frequency band cannot represent a frequency exactly
  - Finite amount of bands in DFT so not everything is perfectly representable
  - Can appear as tails

---
Windowing functions
- Reduce spectral leakage by using a windowing function
  - Multiply input signal by windowing signal then compute DFT
- Side effect: Can broaden the peaks of frequencies in DFT
- Gradually reduce samples at edges of input to DFT to 0 to make signal look periodic (as DFT assumes)
- Many types of windowing functions with tradeoffs between spectral leakage (tails), frequency resolution (main lobes), and amplitude of frequency components

---
Frequency Response of Systems
- Frequency response – DFT of impulse response
- Not readily apparent what impulse response does in time domain, but frequency response makes it easy to see it is a band pass filter
- Impulse response is discrete, but frequency response can be infinitely long if padded with infinite zeroes

---
Convolution via Frequency Domain
- Convolution in time domain is equivalent to multiplication in the frequency domain
  - And vice versa
- What use is this?
  - Deconvolution – Not very doable in time domain. It is just division in the frequency domain though.
  - Performance of convolution
    - Take FFT of both signals, multiply, then take IFFT.
    - Don’t bother doing this with a normal DFT algorithm. The FFT is stupid fast / efficient so it reduces work to do a convolution by a lot

---
How to math (in rectangular)
x

---
How to math (in polar)
- Multiplication
  - Mag Y[f] = Mag X[f] × Mag H[f]
  - Phase Y[f] = Phase X[f] + Phase H[f]
- Division
  - Mag H[f] = Mag Y[f] / Mag X[f]
  - Phase H[f] = Phase Y[f] - Phase X[f]

---
Circular Convolution
- Result of convolution is signal of length N+M-1
- If you do time domain convolution in frequency domain, you must make sure the length of the IDFT is going to be atleast N+M-1
  - Or else you get circular convolution, where adjacent periods spill over into your period